Seebo Mini project
12 November 2014
Jin Kim

1. Development Goal
When SeeboMini system boot up, direct load xbmc 12.2 without Androiod UI

2. Target board : Amlogic M8
2.1 CPU - Amlogic s802, Quad core cortex A9
2.2 GPU- Mali-450
2.3 RAM - 2G
2.4 ROM - 8G
2.5 OS - Android 4.4.2

3. Compare Firmware
	Factory f/w	Amlinux	Openelec	SeeboMini
ROM type	Static(commercial)	Custom	Custom	Custom
Code / Based on	Amlogic / M8-k200	Amlogic / M8-k200	Amlogic / M8-k200	Amlogic / M8-k200
OS	Android 4.4.2	Android 4.4.2	Openelec 4.0.2	Android 4.4.2
Linux kernel	3.10.54	3.10.58	3.10.33	3.10.53
XBMC	13.1(apk type)	13.1 / 13.2	13.2	13.2
Distributor	Default	Stane's 1983	Codesnake	N/A
Source	N/A	N/A	N/A	Yes
Firmware	Yes	Yes	Yes	No
Update / Method	OTA package / (Update.zip)	OTA package / (Update.zip)	OTA package / (Update.zip)

* OTA(Over The Air) package Directory tree
Dir:	META-INF	# updater-script
Dir:	system	# root file system
file:	bootloader.img	# bootloader image file
file:	logo.img	# booting logo
file:	boot.img	# kernel + ramdisk file + device tree file

4. Image files as a result – Meson8-k200 : board name
4.1. Download sources file from http://openlinux.amlogic.com:8000/download/ARM/
4.2. Kernel build with meson8_defconfig ---------------------------> uImage
4.3. Bootloader build (uboot) -----------------------------------------> u-boot.bin
4.4. Filesystem build with Buildroot
---------->	rootfs.cpio	: ramdisk
 m8.dtb	: device tree file
rootfs.tar	: root file system (+ xbmc)
4.5. make OTA package for updating using recovery-aml.mk
4.6. Copy to SD card and insert SD card to the target board
4.7. Reboot in recovery mode
* Buildroot - Buildroot is a set of Makefiles and patches that makes it easy to generate a complete embedded Linux system. Buildroot can generate any or all of a cross-compilation toolchain, a root file system, a kernel image and a bootloader image. Buildroot is useful mainly for people working with small or embedded systems, using various CPU architectures (x86, ARM, MIPS, PowerPC, etc.) : it automates the building process of your embedded system and eases the cross-compilation process.
* recovery-aml.mk – This is makefile script for OTA package for Android device

5. How to build
5.1. Bootloader
Source	: http://openlinux.amlogic.com:8000/download/ARM/u-boot/uboot-2014-08-24-64ca74bb22.tar.gz
Location	: jin@SEEBO-RS300-E6-PS2:~/kernel/jkuboot/uboot-2014
Compile	: make m8_k200_v1_config CROSS_COMPILER=arm-none-eabi-
 make -j16
Result file	: jin@SEEBO-RS300-E6-PS2:~/kernel/jkuboot/uboot-2014/build/u-boot.bin

5.2. Kernel
Source(3.10.33) : http://openlinux.amlogic.com:8000/download/ARM/kernel/arm-src-kernel-2014-08-24-ffa91141da.tar.gz
Source(3.10.53) : https://github.com/Stane1983/amlogic-m6_m8
Location	: jin@SEEBO-RS300-E6-PS2:~/kernel/m8s802/kernel310-53
Compile	: make meson8_defconfig
 make uImage -j16
Result file	: jin@SEEBO-RS300-E6-PS2:~/kernel/m8s802/kernel310-53/arch/arm/boot/uImage
5.2.1. boot.img
Location	: jin@SEEBO-RS300-E6-PS2:~/kernel/pre-built/common/bootimg/mk_bootimag.sh
* Copy your compiled uImage into Location directory, then execute “./mk_bootimg.sh”
Result	: In same directory, boot.img = rootfs.cpio+uImage+m8_jg.dtb

5.3. File system ( xbmc 12.3~13.2 can be selected)
Source	: https://github.com/CoreTech-Development/buildroot-mx_linux
Location	: jin@SEEBO-RS300-E6-PS2:~/buildroot-mx_linux
Compile	: make mx_linux_jynxm6_defconfig
 make menuconfig
 make
 edit some configs – pre-built kernel (3.10.33 / 53 / 58)
* to include bootloader, input string like this “/home/jin/kernel/pre-built/common/bootloader/your u-boot img file at Filesystem images/Advanced option
* pre-built kernel location = ~kernel/pre-built/
Result file	: /home/jin/buildroot-mx_linux/output/image/SeeboMini-update.zip